## Slide 1: CocoSketch: High-Performance Sketch-based Measurement over Arbitrary Partial Key Query
Yinda Zhang1,3, Zaoxing Liu2, Ruixin Wang1, Tong Yang1, Jizhou Li1,
Ruijie Miao1, Peng Liu1, Ruwen Zhang1, Junchen Jiang3
1Peking University, 2Boston University, 3University of Chicago

## Slide 2: Applications need network measurement
Measurement
Data
Traffic Engineering?
Flow Scheduling?
5-tuple?
(SrcIP, DstIP)?
Key: combination of packet-header fields
5-tuple: {SrcIP, DstIP, SrcPort, DstPort, Protocol}

## Slide 3: Applications need measurement over multiple keys
Measurement
Data
DDoS detection
How to locate the attack?
SrcIP? DstIP? 5-tuple?
(IP, port, protocol)?
(SrcIP/28, DstIP/24)?
Other applications:
rule management, rate limiting, …

## Slide 4: Ideally, we want to support arbitrary partial key queries
Measurement
Data
Before measurement:
5-tuple is the full key
After measurement:
query partial key of 5-tuple
e.g., (SrcIP/28, DstIP/16)
1. Support queries on
multiple keys
2. Without the need to predefine each key
Key benefit

## Slide 5: However, prior sketches focus on single keys (UnivMon [SIGCOMM‘16], Elastic Sketch [SIGCOMM‘18], NitroSketch [SIGCOMM’19])
1. I need the statistics
over SrcIP
2. Configure sketch to measure over SrcIP
3. Provide approximate
statistics over SrcIP
1. bounded error rates
2. high throughput
3. small memory usage
Can we reuse them?
Benefits of sketches

## Slide 6: Strawman 1: one single-key sketch per key (SCREAM [CoNEXT‘15], UnivMon [SIGCOMM‘16], RHHH [SIGCOMM‘17])
I may need the
statistics over
SrcIP/16,
SrcIP/20,
SrcIP/24,
……
Configure
sketch1 for SrcIP/16,
sketch2 for SrcIP/20,
sketch3 for SrcIP/24,
……
Resource Name | Percentage
Computing resource for one single-key sketch (Hash Distribution Unit) | 20.83%
Storage resource for one single-key sketch (Map RAM) | 7.11%
Hardware platforms only support
limited single-key sketches
Too many resources needed

## Slide 7: Strawman 2: one single-key sketch for full key
We can recover the statistics
of each key from that of the full key
SrcIP/24 | SrcIP (full key)
…… | ……
56.49.82.* | 56.49.82.0
 | ……
 | 56.49.82.255
…… | ……
Low accuracy for partial keys
Chart: 
| SrcIP/32 (Full Key) | SrcIP/24 (Partial Key)
 | 0.1333 | 0.94089
0.13
0.94
Relative Error for SrcIP/24
Recovered
from SrcIP
Single-key
sketch

## Slide 8: Reusing single-key sketches does not work
Any better solutions to achieve all requirements?
Strawman | Fidelity | Efficiency | Compatibility
Sketch per key |  |  | 
Full-key sketch |  |  | 
Our Target |  |  | 
Strawman | Fidelity | Efficiency | Compatibility
Sketch per key |  |  | 
Full-key sketch |  |  | 
Our Target |  |  | 
Fidelity: Accuracy guarantees over all partial key queries
Efficiency: High throughput using small memory footprints
Compatibility: Work on both software and hardware platforms

## Slide 9: Subset Sum Estimation fits our goal of fidelity
The size of a partial-key flow the sum of a subset of full-key flows
SrcIP/24 (Partial Key)
56.49.82.*
SrcIP (Full Key)
56.49.82.0
56.49.82.1
……
56.49.82.254
56.49.82.255
To achieve fidelity, we should minimize the variance sum of all full-key flows

## Slide 10: State-of-the-art of subset sum estimation (Unbiased SpaceSaving [SIGMOD’18])
Packet
Full Key:
Insert to the bucket with minimum collisions with other full-key flows
Full Key | Size
 | 18
 | 2
…… | ……
 | 13
Full Key | Size
 | 18
 | 2
…… | ……
 | 13
If the full key is recorded,
insert to the corresponding bucket
Unbiased SpaceSaving (USS)

## Slide 11: State-of-the-art of subset sum estimation (Unbiased SpaceSaving [SIGMOD’18])
Packet
Insert to the bucket with minimum collisions with other full-key flows
Full Key | Size
 | 19
 | 2
…… | ……
 | 13
Full Key | Size
 | 19
 | 2
…… | ……
 | 13
Full Key:
If the full key is not recorded,
insert to the bucket with minimum size
replace full key with probability
Unbiased SpaceSaving (USS)

## Slide 12: Can we reuse USS for arbitrary partial key queries?
No, USS falls short on system performance.
Our approach (CocoSketch1) aims to achieve
good system performance while keeping fidelity.
1 Cornucopia Sketch

## Slide 13: 1st Limitation of USS: It needs too many memory accesses
Check all buckets to find the one with minimum collisions
USS with N buckets
Check/Update
Check/Update
Check/Update
……
Full Key | Size
 | 18
 | 2
…… | ……
 | 13
Full Key | Size
 | 18
 | 2
…… | ……
 | 13
Packet
Full Key:

## Slide 14: Technique 1: Stochastic Variance Minimization
Insert to the bucket with minimum collisions among all buckets
hash-indexed
Packet
Map to buckets by hash functions ()

## Slide 15: Setting to 2 or 3 is sufficient
Insight: 2 or 3 accesses can retain similar accuracy
under heavily skewed flow distribution
Throughput
Relative Error
Better
USS

## Slide 16: Why is sufficient?
93 | 49 | 23 | 13 | 13 | 13 | 13 | 12
93 | 49 | 23 | 13 | 13 | 13 | 13 | 12
USS
Key
Size
Large flows: low collision rates
Small flows: collisions are balanced
Chart: 
Size
Rank of size
Update the bucket with minimum collisions
Distribution of size in the bucket

## Slide 17
Chart: 
Power of two choices: In two accesses, we can also balance the collisions well
(DRILL [SIGCOMM’17], DistCache [FAST’19], CHEETAH [NSDI’20])
Large flows: low collision rates
Small flows: collisions are balanced
93 | 49 | 23 | 13 | 13 | 13 | 13 | 12
93 | 49 | 23 | 13 | 13 | 13 | 13 | 12
Key
Size
Size
Distribution of size in the bucket
  Why is sufficient?
Avoid collisions
with large flows
Rank of size

## Slide 18: 2nd Limitation of USS: We cannot implement USS efficiently in hardware platforms
Circular dependencies are incompatible with
the pipeline workflow of hardware platforms
Flow A: (Full Key, Size)
Flow B: (Full Key, Size)
Circular dependencies: the update of variables depends on each other
A<B?
B<A?
FPGA: low clock frequency
Tofino switch: not feasible

## Slide 19: Technique 2: Removing Circular Dependencies
1 Stochastic Variance
Minimization on buckets
buckets
1 buckets
……
1 buckets
independent Stochastic Variance
Minimizations, each on 1 bucket
Packet
Packet
Packet
Report the median result
among buckets
Flow A
Flow B
Flow A
Flow B

## Slide 20: Summary of CocoSketch
Basic CocoSketch: for software platforms (CPU, Open vSwitch)
Hardware-friendly CocoSketch: for hardware platforms (FPGA, Tofino switch)
Stochastic Variance Minimization
+ Circular Dependency Removal
CocoSketch also achieves fidelity as that of USS:
all partial keys share the same accuracy guarantee

## Slide 21: Evaluation Setup
Real-world traces: CAIDA, MAWI
Tasks: heavy hitters, heavy changes, hierarchical heavy hitters
Platforms: Intel CPU, OVS with DPDK, Xilinx FPGA, Barefoot Tofino

## Slide 22: CocoSketch estimates flow size more accurately
Heavy hitter detection in 500KB memory
 | SpaceSaving | UnivMon | Elastic Sketch | CocoSketch (Ours)
Recall rate for single key | 0.935 | 0.987 | 0.984 | 0.985
Recall rate for multiple keys1 | 0.337 | 0.167 | 0.683 | 0.964
1 We measure six different keys and report the average recall rate

## Slide 23: CocoSketch achieves higher throughput
Single-thread throughput in CPU (Mpps)
 | SpaceSaving | UnivMon | Elastic Sketch | CocoSketch (Ours)
Throughput for single key | 5.25 | 2.39 | 23.04 | 23.71
Throughput for multiple keys1 | 1.10 | 0.50 | 5.12 | 23.712
2 The insertion of CocoSketch is not influenced by the number of keys queried
1 We report the throughput of measuring six different keys

## Slide 24: CocoSketch uses less resource in hardware platforms
Heavy hitter detection to guarantee 90% F1 Score in Tofino switch
 | Elastic Sketch for 4 keys* | CocoSketch (Ours)
SRAM | 18.33% | 3.75%
Map RAM | 30.56% | 6.25%
Stateful ALU | 75.00% | 6.25%
*We can implement at most 4 Elastic sketches
in the data plane of Tofino switch

## Slide 25: Conclusions
Arbitrary partial key query is needed
Existing single-key sketches are ill-suited
Arbitrary partial key query is a kind of subset sum estimation
Key idea of CocoSketch
  Stochastic Variance Minimization
  Circular Dependency Removal
Source code: https://github.com/yindazhang/CocoSketch